|  | Department of Computer and Mathematical Sciences |  | CS 2401 Assembly Language | 2 |
| --- | --- | --- | --- | --- |

#### Lab 2: Arithmetic Operations of Signed Number in Binary

Objectives:

The main objective of this lab is to learn how to add and subtract signed number in signed and magnitude, 1’s and 2’s complements.

Task 1: Signed and Magnitude System

Note that subtraction is the same as addition with negative number. A process of addition in signed and magnitude is as follows:

- Convert the two numbers to signed and magnitude.

- If the two numbers have the same sign, find the sum of the magnitudes and keep the sign bit.

- If the two numbers have the different signs, find the difference of the magnitudes and keep the sign of the larger magnitude.

Activity 1.1: Perform the following operation in signed and magnitude in 8 bits:  17 + 35

| 00010001 | + |
| --- | --- |
| 00100011 |  |
| 00110100 |  |

Activity 1.2: Perform the following operation in signed and magnitude in 8 bits: (17 + 35

| 10010001 | + |
| --- | --- |
| 00100011 |  |
| 00010010 |  |

Activity 1.3: Perform the following operation in signed and magnitude in 8 bits: (23 ( 44

| 10010111 | + |
| --- | --- |
| 10101100 |  |
| 11000011 |  |

Task 2: 1’s Complement

A process of addition in 1’s complement is as follows:

- Convert the two numbers to 1’s complement.

- Perform addition.

- If there is a carry out, add one to the sum.

Activity 2.1: Perform the following operation in 1’s complement in 8 bits:  17 + 35

| 00010001 | + |
| --- | --- |
| 00100011 |  |
| 00110100 |  |

Activity 2.2: Perform the following operation in 1’s complement in 8 bits: (17 + 35

| 11101110 | + |
| --- | --- |
| 00100011 |  |
| 100010001 1 |  |
| 00010010 |  |

Activity 2.3: Perform the following operation in 1’s complement in 8 bits: (23 ( 44

| 11101000 | + |
| --- | --- |
| 11010011 |  |
| 110111011 1 |  |
| 10111100 |  |

Task 3: 2’s Complement

A process of addition in 2’s complement is as follows:

- Convert the two numbers to 2’s complement.

- Perform addition.

Activity 3.1: Perform the following operation in 2’s complement in 8 bits:  17 + 35

| 00010001 | + |
| --- | --- |
| 00100011 |  |
| 00110100 |  |

Activity 3.2: Perform the following operation in 2’s complement in 8 bits: (17 + 35

| 11101111 | + |
| --- | --- |
| 00100011 |  |
| 100010010 |  |
| 00010010 |  |

Activity 3.3: Perform the following operation in 2’s complement in 8 bits: (23 ( 44

| 11101001 | + |
| --- | --- |
| 11010100 |  |
| 110111101 |  |
| 10111101 |  |

Activity 3.4: Perform the following operation in 2’s complement in 8 bits:

| 10100000 | carry |
| --- | --- |
| 10101001 | + |
| 10110100 |  |
| 101011101 |  |
| 01011101 |  |

Activity 3.5: Is the result in Activity 3.4 correct? If the answer is either yes or no, explain why?

No, since Carry in is not the same as carry out.

Task 4: Hexadecimal System

A Hexadecimal number is a number with base sixteen.

Activity 4.1: Perform the following operation:

| 2A9F6 | + |
| --- | --- |
| D6B58 |  |
| 10154E |  |

Activity 4.2: Perform the following operation:

| D6B58 | - |
| --- | --- |
| 2A9F6 |  |
| AC162 |  |