|  | Department of Computer and Mathematical Sciences |  | CS 3401 Assembly Language | 4 |
| --- | --- | --- | --- | --- |

#### Lab 4: Introduction to MARIE

Objectives:

The main objective of this lab is to get you familiarized with MARIE a simple computer simulator.

The MARIE architecture has the following characteristics:

- Binary, two's complement data representation.

- Stored program, fixed word length data and instructions.

- 4K words of word-addressable main memory.

- 16-bit data words.

- 16-bit instructions, 4 for the opcode and 12 for the address as shown below.

- A 16-bit arithmetic logic unit (ALU).

- Seven registers for control and data movement.

| Figure 1: MARIE Architecture | Figure 2: MARIE Instruction set |
| --- | --- |

MARIE’s seven registers are:

- Accumulator, AC, a 16-bit register that holds a conditional operator (e.g., "less than") or one operand of a two-operand instruction.

- Memory address register, MAR, a 12-bit register that holds the memory address of an instruction or the operand of an instruction.

- Memory buffer register, MBR, a 16-bit register that holds the data after its retrieval from, or before its placement in memory.

- Program counter, PC, a 12-bit register that holds the address of the next program instruction to be executed.

- Instruction register, IR, which holds an instruction immediately preceding its execution.

- Input register, InREG, an 8-bit register that holds data read from an input device.

- Output register, OutREG, an 8-bit register, that holds data that is ready for the output device.

Task 1: Micro-operations -- Register Transfer Language (RTL)

The exact sequence of micro-operations that are carried out by an instruction can be specified using register transfer language (RTL). In the MARIE RTL, it uses the notation M[X] to indicate the actual data value stored in memory location X, and ( to indicate the transfer of bytes to a register or memory location.

For example the Load X instruction

MAR ( X

MBR ( M[MAR]

AC ( MBR

Activity 1.1: What is the RTL for the Add X instruction?

MAR ( X

MBR ( M[MAR]

AC ( AC + MBR

Activity 1.2: What is the RTL for the Subt X instruction?

MAR ( X

MBR ( M[MAR]

AC ( AC - MBR

Activity 1.3: What is the RTL for the JnS X instruction?

MBR ( PC

MAR ( X

M[MAR] ( MBR

MBR ( X

AC ( 1

AC ( AC + MBR

PC ( AC

Activity 1.4: What is the RTL for the AddI X instruction?

MAR ( X

MBR ( M[MAR]

MAR ( MBR

MBR ( M[MAR]

AC ( AC + MBR

Task 2: Instruction Processing

An instruction is executed as follows:

- The fetch-decode-execute cycle is the series of steps that a computer carries out when it runs a program.

- We first have to fetch an instruction from memory, and place it into the IR.

- Once in the IR, it is decoded to determine what needs to be done next.

- If a memory value (operand) is involved in the operation, it is retrieved and placed into the MBR.

- With everything in place, the instruction is executed.

Activity 2.1: Suppose the location X in a Load X instruction is 104 which contains the value of 35d and the instruction stored at 100 in the memory, complete the following table:

| Step | RTN | PC | IR | MAR | MBR | AC |
| --- | --- | --- | --- | --- | --- | --- |
| (initial values) |  | 100 |  |  |  |  |
| Fetch | MAR ( PC | 100 |  | 100 |  |  |
|  | IR ( M[MAR] | 100 | 1104 | 100 |  |  |
|  | PC ( PC + 1 | 101 | 1104 | 100 |  |  |
| Decode | MAR ( IR[11-0] | 101 | 1104 | 104 |  |  |
|  | (decode IR[15-12]) | 101 | 1104 | 104 |  |  |
| Get operand | MBR ( M[MAR] | 101 | 1104 | 104 | 0023 |  |
| Execute | AC ( MBR | 101 | 1104 | 104 | 0023 | 0023 |

Activity 2.2: Suppose the location X in an ADD X instruction is 105 which contains the value of (23d and the instruction stored at 101 in the memory, complete the following table:

| Step | RTN | PC | IR | MAR | MBR | AC |
| --- | --- | --- | --- | --- | --- | --- |
| (initial values) |  | 101 | 1104 | 104 | 0023 | 0023 |
| Fetch | MAR ( PC | 101 | 101 | 101 | 0023 | 0023 |
|  | IR ( M[MAR] | 101 | 3105 | 101 | 0023 | 0023 |
|  | PC ( PC + 1 | 102 | 3105 | 101 | 0023 | 0023 |
| Decode | MAR ( IR[11-0] | 102 | 3105 | 105 | 0023 | 0023 |
|  | (decode IR[15-12]) | 102 | 3105 | 105 | 0023 | 0023 |
| Get operand | MBR ( M[MAR] | 102 | 3105 | 105 | FFE9 | 0023 |
| Execute | AC ( AC + MBR | 102 | 3105 | 105 | FFE9 | 000C |

Activity 2.3: Suppose the location X in a Store X instruction is 106 and the instruction stored at 102 in the memory, complete the following table:

| Step | RTN | PC | IR | MAR | MBR | AC |
| --- | --- | --- | --- | --- | --- | --- |
| (initial values) |  | 102 | 3105 | 105 | FEE9 | 000C |
| Fetch | MAR ( PC | 102 | 3105 | 102 | FFE9 | 000C |
|  | IR ( M[MAR] | 102 | 2106 | 102 | FFE9 | 000C |
|  | PC ( PC + 1 | 103 | 2106 | 102 | FFE9 | 000C |
| Decode | MAR ( IR[11-0] | 103 | 2106 | 106 | FFE9 | 000C |
|  | (decode IR[15-12]) | 103 | 2106 | 106 | FFE9 | 000C |
| Get operand |  | 103 | 2106 | 106 | FFE9 | 000C |
| Execute | MBR ( AC | 103 | 2106 | 106 | 000C | 000C |
|  | M[MAR] ( MBR | 103 | 2106 | 106 | 000C | 000C |

Task 3: MARIE Assembly Program

Activity 3.1: Enter the following assembly code in MARIE Assembly Code Editor and save.

Load X

Subt Y

Skipcond 000

Jump Else

Then, Load Y

Subt X

Store Y

Jump Endif

Else, Load X

Subt Y

Store X

Endif, Halt

X, DEC 20

Y, DEC 30

Activity 3.2: Assemble the program, then debug or run the program in MARIE Simulator.

Activity 3.3: What is the content at location of X and Y at end of the program?

| Location | Content |
| --- | --- |
| X | 0014 |
| Y | 000A |

Activity 3.4: Replace the instruction X, DEC 20 by X, DEC 40. What is the content at location of X and Y at end of the program?

| Location | Content |
| --- | --- |
| X | 000A |
| Y | 001E |

Activity 3.5: Describe what the program in Activity 3.1 does.

if (X - Y) < 0 Y = Y – X else X = X - Y

Activity 3.6: Convert each instruction in the following program to its corresponding machine code in hex.

| Location | Instruction | Machine Code |
| --- | --- | --- |
| 000 | Load X | 100C |
| 001 | Subt Y | 400D |
| 002 | Skipcond 000 | 8000 |
| 0003 | Jump Else | 9008 |
| 004 | Then, Load Y | 100D |
| 005 | Subt X | 400C |
| 006 | Store Y | 200D |
| 007 | Jump Endif | 900B |
| 008 | Else, Load X | 100C |
| 009 | Subt Y | 400D |
| 00A | Store X | 200C |
| 00B | Endif, Halt | 7000 |
| 00C | X, DEC 20 | 0014 |
| 00D | Y, DEC 30 | 001E |